## Slide 1: Highres BioSolutions Programming Challenge
Nick Hinchliffe

## Slide 2: Problem Description
Implement DeviceDriver:
OpenConnection(string IPAddress)
Initialize()
ExecuteOperation(string operation, string[] parameterNames, string[] parameterValues)
Abort()
Notes: Problem Description: Implement a DeviceDriver which will allow a user to control a MockRobot by a set of specified commands. User will press a button mapped to one of the DeviceDriver functions after typing in any needed parameters.
OpenConnection -> Create TCP/IP connection between UI and MockRobot through the DeviceDriver.
Initialize -> Put MockRobot into an automation-ready (homed) state.
ExecuteOperation -> DeviceDriver will perform an operation determined by the parameter operation
Can be: Pick, Place, and Transfer.
Abort -> Expects that DeviceDriver will terminate communication with the MockRobot.

## Slide 3: MockRobot Device API
Given accepted commands:
home
pick
place
status
Notes: These API commands are how the DeviceDriver interacts with the robot.
These are given, the robot will understand them when they are given as a string with a % sign before any parameters.
Home puts the robot in a homed, automation ready state
Pick will pick up an object from a given Source location, int parameter
Place will place an object which the Robot will already be holding at a Destination location, int parameter
Status checks the status of command specified by it’s PID. Will return: In Progress, Finished Successfully, and or Terminated with Error

## Slide 4: System Architecture
Client Server Architecture

## Slide 5: Implementation
Methods:
OpenConnection(String IPAddress)
Abort()
Initialize()
  checkInitResults(int initPid, String res)
  checkBot(int pid)
ExecuteOperation(string operation, string[] parameterNames, string[] parameterValues)
  pick/place(string location, string res, int pid, string lastOperation)
  transfer(string[] parameterNames, string[] parameterValues, string res, int pid, string lastOperation)
  isValid(string operation, string[] parameterNames, string[] parameterValues)
  checkMockBotStatus(int pid, String res)
  checkBot(int pid)

## Slide 6: “Global” variables
Private
Non static
Null, false, or empty
Accessible

## Slide 7: Open Connection

## Slide 8: Abort

## Slide 9: Initialize

## Slide 10: Check Init Results

## Slide 11: Check bot

## Slide 12: Execute operation

## Slide 13: iS Valid

## Slide 14: iS Valid Activity Diagram

## Slide 15: Pick & place

## Slide 16: Check mock Bot status

## Slide 17: Transfer

## Slide 18: challenges
Time Management
Depth of Project
Reviewing Socket Programming in Java
Creating logic for checking Bot

## Slide 19: Future improvements
Implement methods as boolean
Create a MockBot
Finding a better way to get pid from Mockbot
More dynamic code
Notes: Have enum to return codes from

## Slide 20: Lessons Learned
More about Automation Engineer Position
Logic behind robot automation
Socket Programming in java
Improved prioritizing skills
Notes: Have enum to return codes from

## Slide 21: Conclusion
Notes: Automation Engineer

## Slide 22: Questions?

## Slide 23: Image sources
https://www.titian.co.uk/highres-biosolutions
https://medium.com/@sgg2123/apis-and-ruby-7675144f3391
https://medium.com/corda/how-to-develop-a-blockchain-application-if-you-only-know-java-f93dcf52cb60
https://knowlab.in/dont-limit-your-challenges-challenge-your-limits/
https://digest.bps.org.uk/2018/03/21/is-the-future-ahead-not-for-those-born-blind/
https://www.sourcecon.com/closing-out-2018-with-lessons-learned-on-the-job/
https://twitter.com/highresbio
Notes: Automation Engineer